## Slide 1: Assessing the resistive capabilities of urban environments to an inundating Tsunami
1st graduate rotation
Nick Dando
RAMP

## Slide 2: Realistic hydrodynamic behaviour of model
The resistive capabilities of the small obstacles play an important role in resisting the inundating wave
Currently implementation of many small object in ANUGA is computational expensive

## Slide 3: Project aims and outputs
Outputs
  Range of friction values to represent urban scenarios
Research paths
  Method of comparison and measurement
  Urban environment variables: what are they?
  Match friction values and determine their suitability.

## Slide 4: Heavy Model Maths
LHS: Volume and Momentum conservation
RHS: Forcing terms, gravity and friction
U conservation of volume within cell over time
E and G deals with fluxes between cells
S0 gravity forcing term
S1 friction forcing term

## Slide 5: Open Channel Flow and Friction
Primarily derived to help with open channel flow problems
Manning formula calculates equivalent friction bedslope
Sf = Equivalent bedslope friction
V = Water volume velocity
h = Water depth of cell
n = empirically derived friction coefficient.
(0.005 – 0.5)
flow
Friction surface
Sf
Sb
Steady state is reached when Sf = Sb

## Slide 6: Model set up: Open channel flow
200m
Breadth
200m
WAVE
building/
friction zone
Length = 1000m
WAVE
buildings
zone
Friction
zone
WAVE
Water Depth
Cross Section
Water Depth
Cross Section

## Slide 7: Selection of friction value
Relative RMS test compared friction and building water levels
Many friction scenarios were compared to a candidate friction scenario
Matched value was deemed to have the lowest RMS value
11 points were used to compare stage levels at a specific time interval

## Slide 8: 20m wave best fit friction values
Best fit friction value is chosen by the minimum of the curves

## Slide 9: Building orientations and layouts
These four scenarios were thought to provide the best and worst cases for the inundating wave
Straight:
No rotation
No offset
Straight offset:
No rotation
‘perfect’ offset
Rotated:
45° rotation
No offset
Rotated Offset:
45° rotation
‘perfect’ Offset

## Slide 10: 20m wave best fit friction values

## Slide 11: 20m wave best fit friction values

## Slide 12: Building parameters: Conclusions
Friction selection behaves as expected
Important factors:
  Width/building density
  Rotation
  Offset
Difficulty in measuring these parameters However building density can be used as base friction values.

## Slide 13: Tsunami variables
Further investigation:
  Inundation time varies
    Wave period
    Distance from shore
  Water depths affected by
    Inundating wave height
    Topographic affects
Determine how changes affect results
  Datum analysis

## Slide 14: Inundation behaviour
For most cases: Friction slower than building inundation
For all matched friction values
Gets worse for smaller wave heights.
Indicates different hydrodynamic behaviour.

## Slide 15: Changes in wave height

## Slide 16: Changes in inundation time

## Slide 17: Datums and their uses:

## Slide 18: Why it doesn’t work
Particular inundation times for Tsunamis
  100 - 1000 seconds
  Inner or last parts: Small inundation times
Spatially varying water depths due to topography
Fundamental different hydrodynamic effects on the inundating water.

## Slide 19: Recommendations
Friction doesn’t reach steady state within Tsunami period we are looking at
Underestimate friction values is better than overestimating friction values.
This is what leads to the large errors.